Enable robot

Robot State

Topic : /robot/state
Msg : baxter_core_msgs/AssemblyState

uint8 ESTOP_BUTTON_UNPRESSED=0
uint8 ESTOP_BUTTON_PRESSED=1
uint8 ESTOP_BUTTON_UNKNOWN=2
uint8 ESTOP_BUTTON_RELEASED=3
uint8 ESTOP_SOURCE_NONE=0
uint8 ESTOP_SOURCE_USER=1
uint8 ESTOP_SOURCE_UNKNOWN=2
uint8 ESTOP_SOURCE_FAULT=3
uint8 ESTOP_SOURCE_BRAIN=4
bool enabled
bool stopped
bool error
uint8 estop_button
uint8 estop_source

Subscribe to the Robot State for the enabled and error state of the robot hardware itself. It also includes information on the EStop.

Enable Robot

Topic : /robot/set_super_enable

Msg : std_msgs/Bool

bool data

data: true to Enable robot motors; false to disable.
You can check the Robot State Topic to see if the robot enabled properly or if it has an error.

Reset Robot State

Topic : /robot/set_super_reset
Msg : std_msgs/Empty

Publish an Empty message to reset the state after an error.

### Robot Description (URDF)

## Joints
Topic : /robot/joint_states
Msg : sensor_msgs-JointState
std_msgs/Header header
string[] name
float64[] position
float64[] velocity
float64[] effort

where the units for the position of a joint are in (rad), the units of velocity are in (rad/s) and the units of effort in each joint is in (Nm).

### Arm Joints
Component IDs:
left_e0, left_e1, left_s0, left_s1, left_w0, left_w1, left_w2, right_e0, right_e1, right_s0, right_s1, right_w0, right_w1, right_w2

#### Arm Joint States
/robot/joint_states (sensor_msgs-JointState)
- name[i]: '<component_id>' of i-th joint in message value arrays.
- position[i]: position of joint i rad
- velocity[i]: velocity of joint i in rad/s
- effort[i]: effort applied in joint i in Nm
Joint states are published by the robot_state_publisher and are updated with information from the sensors for every cycle.

Set Joint State Publishing Rate
/robot/joint_state_publish_rate (std_msgs-UInt16) uint16 data
Default rate is 100Hz; Maximum is 1000Hz

#### Arm Joint Control
There are currently four modes for controlling the arms: Joint Position Mode, Joint Velocity Mode, and Joint Torque Mode, and 'raw' Joint Position Mode.

Switching Modes

Topic : /robot/limb/<side>/joint_command
Msg : baxter_core_msgs/JointCommand
int32 POSITION_MODE=1
int32 VELOCITY_MODE=2
int32 TORQUE_MODE=3
int32 RAW_POSITION_MODE=4
int32 mode
float64[] command
string[] names

### Collision Avoidance

/robot/limb/right/suppress_collision_avoidance (std_msgs-Empty)
To disable torso self collision avoidance, a std_msgs/Empty message must be published at a rate greater than 5 Hz.

## Cartesian Endpoint
#### Endpoint State

Topic : /robot/limb/<side>/endpoint_state
Msg baxter_core_msgs-EndpointState

geometry_msgs/Pose pose
geometry_msgs/Twist twist

geometry_msgs/Wrench wrench

#### Inverse Kinematics Solver Service

Topic:/ExternalTools/<side>/PositionKinematicsNode/IKService
Srv : baxter_core_msgs/SolvePositionIK.srv

uint8 SEED_AUTO=0
uint8 SEED_USER=1
uint8 SEED_CURRENT=2
uint8 SEED_NS_MAP=3
geometry_msgs/PoseStamped[] pose_stamp
sensor_msgs/JointState[] seed_angles
uint8 seed_mode

uint8 RESULT_INVALID=0
sensor_msgs/JointState[] joints
bool[] isValid
uint8[] result_type